## Slide 1
AMR ROS 2 SOFTWARE ARCHITECTURE
How the simulated mobile
manipulator works
Current-source presentation for the ROS 2 Humble project
Current configuration values are used.
Older report values are labeled historical.
AMR
Sensors
Nav2
MoveIt
Gazebo
ROS 2 Humble • Gazebo Harmonic • simulation scope
Notes: Purpose: introduce the deck as a software architecture explanation.
Say: This project is a ROS 2 Humble and Gazebo Harmonic simulation of an autonomous mobile robot with a mounted manipulator. The deck explains how sensing, localization, navigation, manipulation and safety boundaries work together.
Emphasize: The scope is simulation. The deck describes the current source tree and does not make a hardware or functional-safety claim.
Source basis: AGENTS.md; SESSION_HANDOFF.md; src/README.md

## Slide 2
AMR ROS 2 SOFTWARE ARCHITECTURE
Scope and operating modes
The workspace is a ROS 2 Humble simulation of a factory AMR with a mounted arm. The primary product source set contains 17 packages under src/
PROJECT SCOPE
Mobile base navigation and command safety
Front and rear LiDAR perception
SLAM, localization, exploration and factory missions
KUKA arm, gripper and product transport in simulation
MODE OWNERSHIP
Mapping / exploration
SLAM Toolbox publishes map → odom
Factory localization
AMCL + map server publish map → odom
Manipulation
MoveIt plans the arm; base motion remains separate
Authority boundaries are part of the design: one owner for each command and TF boundary, with stale or unsafe inputs rejected.
Sources: src/README.md; src/amr_bringup/config/interface_ownership.yaml; src/amr_slam/config/mapper.yaml; src/amr_factory/config/amcl.yaml
02
Notes: Purpose: define what the project contains and why the graph has more than one runtime mode.
Explain: The primary project set is the 17 packages under src/. Mapping and exploration use SLAM Toolbox to own map → odom. Factory localization uses AMCL and a saved map to own map → odom. MoveIt handles the arm and gripper while mobile base motion remains under Nav2 and command arbitration.
Key point: TF and command ownership changes by mode, but each active boundary has one owner. That prevents competing transforms and conflicting motion commands.
Source basis: src/README.md; src/amr_bringup/config/interface_ownership.yaml; src/amr_slam/config/mapper.yaml; src/amr_factory/config/amcl.yaml

## Slide 3
AMR ROS 2 SOFTWARE ARCHITECTURE
End-to-end ROS 2 workflow
The program is a data path plus explicit authority gates. Sensor data moves forward; command ownership narrows toward the simulated base
Gazebo
sensors
Sensor
adapters
EKF +
localization
SLAM /
AMCL
Nav2 planner
+ smoother
RPP
controller
Arbitration
+ base
Mission / factory supervisor
NavigateToPose, product cycle, home
MoveIt2
arm and gripper trajectory
Gazebo plant
watchdog + diff drive
State path
wheel + IMU → EKF → odom → base_footprint → Nav2
Command path
RPP → arbitration → base adapter → Gazebo
Sources: src/amr_bringup/config/interface_ownership.yaml; src/amr_navigation/config/planner.yaml; src/amr_mpc_controller/config/controller.yaml
03
Notes: Purpose: show the whole ROS 2 workflow before explaining individual subsystems.
Read the upper path from Gazebo sensors through adapters, state estimation, localization, Nav2, RPP and the base command boundary. The lower branch shows that the mission or factory supervisor sends navigation actions, while MoveIt controls the arm trajectory.
Clarify: The diagram is a simplified teaching view. Sensor and localization streams run in parallel in the actual graph. The exact two-LiDAR routing appears on slide 9.
Key point: Nav2 produces a velocity request. Project-owned arbitration, the base adapter and the Gazebo watchdog decide whether the base can accept motion.
Source basis: src/amr_bringup/config/interface_ownership.yaml; src/amr_navigation/config/planner.yaml; src/amr_mpc_controller/config/controller.yaml

## Slide 4
AMR ROS 2 SOFTWARE ARCHITECTURE
AMR capabilities and operating loop
The AMR combines navigation, perception and manipulation. The factory supervisor turns these subsystems into a guarded product cycle
Sense
LiDAR, IMU, wheel state, product camera
Localize
EKF for odom; SLAM or AMCL for map
Navigate
Planner, smoother and RPP
Manipulate
MoveIt arm/gripper plan and attachment proof
Verify
Freshness, collision, cancellation and terminal gates
Current autonomous factory scope
Product 101 and Product 102 are the active registry-driven scope
Product 103, Gate 7, hardware and functional-safety acceptance are outside scope
Home permission depends on idle, fresh and safe empty-stowed proof
Sources: src/amr_factory/launch/factory_autonomous.launch.py; src/amr_factory/scripts/factory_cli.py; src/amr_bringup/config/interface_ownership.yaml
04
Notes: Purpose: explain what the AMR can do as an operating loop.
Walk through the stages: sensors provide observations; EKF and map localization provide pose; Nav2 plans and follows paths; MoveIt performs arm and gripper actions; supervisors verify freshness, collision, cancellation and terminal state.
Scope note: the current registry-driven autonomous factory scope is Product 101 and Product 102. Product 103, Gate 7, physical hardware and functional-safety acceptance remain outside the documented scope.
Source basis: src/amr_factory/launch/factory_autonomous.launch.py; src/amr_factory/scripts/factory_cli.py; src/amr_bringup/config/interface_ownership.yaml

## Slide 5
AMR ROS 2 SOFTWARE ARCHITECTURE
Robot model: URDF and Xacro
Xacro builds the robot description once and reuses it across Gazebo, TF, sensor adapters, Nav2 and MoveIt
map
odom
base_footprint
base_link
front_lidar_link
rear_lidar_link
imu_link
arm_base_link → arm_* → gripper_tcp
product_camera_optical_frame
amr.urdf.xacro
Chassis, drive wheels, casters, LiDARs and IMU
Gazebo DiffDrive plus native command watchdog
CAD visuals with primitive collision geometry
phase14_mobile_manipulator.urdf.xacro
Includes the base description and KUKA KR6 R900-2 macro
Adds gripper, product camera, optional loaded product and attachment hooks
Uses gz_ros2_control for arm and gripper joint interfaces
Sources: src/amr_description/urdf/amr.urdf.xacro; src/amr_description/urdf/phase14_mobile_manipulator.urdf.xacro
05
Notes: Purpose: connect the robot model to TF, sensors, Gazebo and MoveIt.
Explain: amr.urdf.xacro defines the base, wheels, casters, LiDAR links, IMU link and Gazebo base plugins. phase14_mobile_manipulator.urdf.xacro includes that base and adds the KUKA KR6 R900-2 arm, gripper, product camera, optional product and attachment interfaces.
Read the TF chain as map → odom → base_footprint → base_link. The sensor and arm frames branch from base_link. The robot description defines the physical relationships; SLAM, AMCL and EKF publish the runtime transforms.
Source basis: src/amr_description/urdf/amr.urdf.xacro; src/amr_description/urdf/phase14_mobile_manipulator.urdf.xacro; src/amr_manipulation/launch/move_group.launch.py

## Slide 6
AMR ROS 2 SOFTWARE ARCHITECTURE
Sensors and ROS interfaces
Adapters give each simulated sensor a stable project-owned topic and preserve the sensor frame. Consumers subscribe to the interface they own
Source | Project interface | Main consumer
Front LiDAR | /amr/sensors/front_lidar/scan /amr/sensors/front_lidar/points | SLAM Toolbox front perception
Rear LiDAR | /amr/sensors/rear_lidar/scan /amr/sensors/rear_lidar/points | rear perception local + global costmaps
IMU | /amr/sensors/imu/data_raw | robot_localization EKF
Base / wheel state | /amr/base/odometry_raw /amr/base/joint_states | wheel odometry MoveIt / controllers
Product camera | /amr/sensors/product_camera/* | AprilTag / manipulation
Sensor streams use sensor QoS. The perception pipeline drops malformed, stale, future or non-monotonic point clouds before republishing accepted data.
Source: src/amr_bringup/config/interface_ownership.yaml; src/amr_sensor_adapters/src; src/amr_perception/src/lidar_pipeline_node.cpp
06
Notes: Purpose: show the stable ROS interfaces between simulated sensors and consumers.
Explain each row: the front scan feeds SLAM and the front perception path; the rear point cloud feeds rear perception and both costmaps; IMU data goes to the EKF; base odometry and joint states support localization, controllers and MoveIt; camera topics support product perception.
Important detail: the adapter layer gives the rest of the system project-owned topic names and preserves the sensor frame. The perception pipeline rejects malformed, stale, future or non-monotonic clouds.
Source basis: src/amr_bringup/config/interface_ownership.yaml; src/amr_sensor_adapters/src/lidar_adapter_node.cpp; src/amr_perception/src/lidar_pipeline_node.cpp

## Slide 7
AMR ROS 2 SOFTWARE ARCHITECTURE
Sensor fusion: how the EKF helps
The EKF produces a planar, time-bounded odometry estimate for local motion. It does not decide the global map position
Wheel odometry
/amr/localization/wheel_odometry
IMU
/amr/sensors/imu/data_raw
yaw + yaw rate
robot_localization
ekf_filter_node
Fused odometry
/amr/localization/odometry
TF: odom → base_footprint
CURRENT EKF CONTRACT
2D filter, world_frame: odom
30 Hz, 0.2 s sensor timeout
Wheel velocity plus IMU yaw / yaw rate
Reset on time jump
Source: src/amr_localization/config/ekf.yaml; src/amr_localization/test/test_localization_contract.py
07
Notes: Purpose: explain what sensor fusion means in this project.
The EKF combines wheel odometry with IMU yaw and yaw rate. It runs as a planar filter at 30 Hz, uses a 0.2 second sensor timeout and publishes the fused odometry topic plus odom → base_footprint.
Explain the boundary: this improves the local motion estimate used by controllers and navigation. It does not build a map or decide the robot’s global map position. SLAM Toolbox or AMCL supplies the separate map → odom relationship.
Source basis: src/amr_localization/config/ekf.yaml; src/amr_localization/launch/amr_localization.launch.py; src/amr_bringup/config/interface_ownership.yaml

## Slide 8
AMR ROS 2 SOFTWARE ARCHITECTURE
Localization and TF ownership
Both localization modes share the same local odometry TF. They differ in who owns map → odom
map
odom
base_footprint
MAPPING / EXPLORATION
SLAM Toolbox owns map → odom
Front LaserScan + odometry
FACTORY LOCALIZATION
AMCL + map server own map → odom
Saved map + odometry
The single-owner TF rule prevents SLAM and AMCL from publishing competing global transforms in the same runtime mode.
Source: src/amr_bringup/config/interface_ownership.yaml; src/amr_slam/config/mapper.yaml; src/amr_factory/config/amcl.yaml
08
Notes: Purpose: explain localization as a TF ownership problem.
Both modes use the same chain from odom to base_footprint. In mapping or exploration, SLAM Toolbox uses the front scan and odometry to build the map and publish map → odom. In factory mode, AMCL matches the saved map using sensor observations and odometry and publishes map → odom.
Key point: SLAM and AMCL must not publish the global transform at the same time in one runtime mode. The interface ownership contract makes the active owner explicit.
Source basis: src/amr_bringup/config/interface_ownership.yaml; src/amr_slam/config/mapper.yaml; src/amr_factory/config/amcl.yaml; src/amr_localization/config/ekf.yaml

## Slide 9
AMR ROS 2 SOFTWARE ARCHITECTURE
Two LiDARs and SLAM Toolbox
The current design keeps LiDAR streams separate. SLAM Toolbox consumes the front LaserScan; both adapted point clouds feed Nav2 obstacle layers
Front LiDAR
scan + points
front_lidar_link
Rear LiDAR
scan + points
rear_lidar_link
SLAM Toolbox
front LaserScan
map → odom
Independent perception
front points + rear points
accepted clouds keep source frames
Nav2 obstacle layers
front_points + rear_points
marking and clearing
No direct front + rear scan concatenation is configured for SLAM Toolbox. Separation comes from distinct topics, frames, adapters and consumers.
Sources: src/amr_slam/config/mapper.yaml; src/amr_slam/launch/amr_slam.launch.py; src/amr_navigation/config/planner.yaml; src/amr_perception/src/lidar_pipeline_node.cpp
09
Notes: Purpose: answer the two-LiDAR question precisely.
The current implementation does not concatenate the front and rear scans into one scan for SLAM Toolbox. SLAM Toolbox consumes the front LaserScan. The front and rear adapted PointCloud2 streams go through separate perception pipelines and then enter Nav2 obstacle layers as front_points and rear_points.
Explain why this does not interfere: the sensors have distinct topics and frames, each adapter preserves the source frame, the perception nodes have no motion authority, and stale or future clouds are rejected.
Source basis: src/amr_slam/config/mapper.yaml; src/amr_slam/launch/amr_slam.launch.py; src/amr_sensor_adapters/src/lidar_adapter_node.cpp; src/amr_perception/src/lidar_pipeline_node.cpp; src/amr_navigation/config/planner.yaml

## Slide 10
AMR ROS 2 SOFTWARE ARCHITECTURE
Nav2: planning and path following
Nav2 converts a navigation goal and the current costmaps into a path, a smoothed path and a velocity request
Mission / factory
NavigateToPose
Planner server
Smac lattice + precision plugins
Smoother server
SimpleSmoother
Controller server
FollowPath / placement
/amr/mpc/cmd_vel
Twist request
CURRENT PLANNER SET
GridBased: nav2_smac_planner/SmacPlannerLattice
ExactGoalLattice: project plugin for exact endpoints
PrecisionGridBased: project PrecisionNavfnPlanner for docking
BOUNDARY
Nav2 requests motion through the controller output topic
Command arbitration owns the accepted base command
Stale or unsafe requests are rejected or stopped
Sources: src/amr_navigation/config/planner.yaml; src/amr_mpc_controller/config/controller.yaml; src/amr_mission/src/mission_supervisor_node.cpp
10
Notes: Purpose: explain what Nav2 contributes.
A mission or factory supervisor sends a NavigateToPose action. The planner server selects a path planner, the smoother server refines the path, and the controller server runs the active FollowPath or placement controller. The output is /amr/mpc/cmd_vel.
Current planner details: GridBased uses SmacPlannerLattice, ExactGoalLattice is project-owned for exact endpoints, and PrecisionNavfnPlanner is project-owned for docking precision. SimpleSmoother is the active smoother.
Key point: Nav2 is responsible for navigation planning and path following. It does not bypass the project-owned command arbitration boundary.
Source basis: src/amr_navigation/config/planner.yaml; src/amr_navigation/precision_planner_plugin.xml; src/amr_mpc_controller/config/controller.yaml

## Slide 11
AMR ROS 2 SOFTWARE ARCHITECTURE
RPP: regulated local control
Regulated Pure Pursuit turns a planned path, the robot pose and local obstacle information into a bounded velocity request
Path
Pose + velocity
Local cost
RPP
lookahead + curvature
collision and speed regulation
/amr/mpc/cmd_vel
Twist request
NORMAL FOLLOWPATH
amr_mpc_controller::HeadingLatchedRPP
0.50 m/s • lookahead 0.30–0.90 m • 1.50 s
PLACEMENT
nav2_regulated_pure_pursuit_controller::RegulatedPurePursuitController
0.10 m/s • reversing allowed for precision placement
Source: src/amr_mpc_controller/config/controller.yaml; src/amr_mpc_controller/include; src/amr_mpc_controller/src
11
Notes: Purpose: explain RPP and its location in the graph.
Regulated Pure Pursuit chooses a lookahead point on the path, converts the path geometry into curvature and scales speed using collision and cost information. It produces a bounded Twist request.
Normal navigation loads amr_mpc_controller::HeadingLatchedRPP with a 0.50 m/s desired speed and velocity-scaled lookahead between 0.30 and 0.90 m. Precision placement uses the native Nav2 RegulatedPurePursuitController at 0.10 m/s and allows reversing for tight placement.
Clarify: the package name contains mpc for compatibility. The current FollowPath plugin is RPP-based; it is not an MPC solver.
Source basis: src/amr_mpc_controller/config/controller.yaml; src/amr_mpc_controller/include; src/amr_mpc_controller/src

## Slide 12
AMR ROS 2 SOFTWARE ARCHITECTURE
Global and local costmaps
Both costmaps model the same padded rectangular robot footprint. Their frames and update behavior match their job
Property | Global costmap | Local costmap
Frame | map | odom
Window | Global map | 5 m × 5 m rolling window
Layers | Static map + obstacles + inflation | Obstacles + inflation
Update / publish | 2 Hz / 1 Hz | 5 Hz / 2 Hz
Sensors | Front + rear PointCloud2 | Front + rear PointCloud2
COST BUILD-UP
Static map
(global only)
Obstacle layer
front_points + rear_points
Inflation
0.75 m, scale 3.0
Planner + controller
query cost and clearance
Footprint: x ±0.60 m, y ±0.40 m, padding 0.01 m
Resolution: 0.05 m
Source: src/amr_navigation/config/planner.yaml; src/amr_mpc_controller/config/controller.yaml
12
Notes: Purpose: distinguish the global and local costmaps.
The global costmap uses map, includes the static map and plans over the larger known environment. The local costmap uses odom, rolls with the robot and reacts quickly to nearby obstacles. Both use front and rear PointCloud2 observations.
Current configuration: 0.05 m resolution, 0.75 m inflation radius, a rectangular footprint of x ±0.60 m and y ±0.40 m with 0.01 m padding. The global map updates at 2 Hz and publishes at 1 Hz; the local window updates at 5 Hz and publishes at 2 Hz.
Key point: costmaps provide collision and clearance information to the planner and controller. They do not own the base command.
Source basis: src/amr_navigation/config/planner.yaml; src/amr_mpc_controller/config/controller.yaml

## Slide 13
AMR ROS 2 SOFTWARE ARCHITECTURE
Command path and safety gates
The base accepts motion only after the request passes the project-owned arbitration and adapter boundaries
RPP
Twist
Arbitration
TwistStamped
Base adapter
/amr/simulation/base/cmd_vel
Gazebo watchdog
native plant input
FAIL-CLOSED PARAMETERS
Source timeout
200 ms
Maximum linear speed
0.50 m/s
Maximum angular speed
0.64 rad/s
Acceleration limits
0.50 m/s² • 0.40 rad/s²
Native watchdog
200 ms
Missing, stale, unsafe or unowned input results in a stop or rejection.
The manipulator-stowed requirement is selected by the active launch/mode.
Source: src/amr_control/config/control.yaml; src/amr_description/urdf/amr.urdf.xacro; src/amr_base_adapter
13
Notes: Purpose: show how a velocity request becomes accepted base motion.
RPP publishes a geometry_msgs/Twist request on /amr/mpc/cmd_vel. The arbitration node applies source freshness, velocity and acceleration limits and publishes a TwistStamped command. The base adapter forwards the approved command to the Gazebo input topic. The native watchdog stops the plant when commands are missing or too old.
Current limits: 0.50 m/s linear, 0.64 rad/s angular, 0.50 m/s² linear acceleration and 0.40 rad/s² angular acceleration. The source and native watchdog timeouts are 200 ms.
Key point: stale, unsafe or unowned motion input fails closed.
Source basis: src/amr_control/config/control.yaml; src/amr_control/src/command_arbitration_node.cpp; src/amr_description/urdf/amr.urdf.xacro; src/amr_base_adapter

## Slide 14
AMR ROS 2 SOFTWARE ARCHITECTURE
Operator commands and control functions
Use the current launch and CLI boundaries. Build first, source the workspace, then start only the mode you need
BUILD AND TEST
source /opt/ros/humble/setup.bash
colcon build --symlink-install
colcon test
colcon test-result --verbose
SIMULATION + TELEOP
ros2 launch amr_simulation amr_simulation.launch.py
ros2 run amr_control prototype_teleop.py
W / S / A / D: move
X or Space: stop • Q: quit
FACTORY AUTONOMOUS
ros2 launch amr_factory factory_autonomous.launch.py control_mode:=autonomous factory_attachment:=true
ros2 launch amr_manipulation move_group.launch.py
FACTORY CLI FUNCTIONS
list
show stations / products
mode autonomous
select autonomous operation
send pickup_a dispatch
run one product route
send pickup_b dispatch
run the second route
loop pickup_a pickup_b --cycles 1
run a bounded sequence
stop / cancel / status
control or inspect the current action
go home
request home only after safe idle proof
Sources: src/README.md; docs/SIMULATION_COMMANDS.md; docs/ROS2_BEGINNER_PROJECT_GUIDE.md
14
Notes: Purpose: give the operator the correct entry points.
Explain the order: source ROS 2 Humble, build and test, source the workspace, launch the simulation, then use teleop or a factory mode. Teleop uses W/S/A/D for movement, X or Space to stop and Q to quit.
For the factory flow, start factory_autonomous.launch.py with autonomous mode and attachment enabled, start MoveIt separately, then use factory_cli.py for list, mode, send, loop, stop, cancel, status and go home. Home is guarded by safe idle and stowed-state proof.
These commands describe the simulation workflow. They do not imply hardware readiness.
Source basis: src/README.md; docs/SIMULATION_COMMANDS.md; docs/ROS2_BEGINNER_PROJECT_GUIDE.md

## Slide 15
AMR ROS 2 SOFTWARE ARCHITECTURE
MoveIt and manipulation
MoveIt plans and executes arm and gripper trajectories. It does not own the mobile base velocity command
MoveIt2
move_group
OMPL planning
Planning scene
robot model + collision objects
product attachment state
gz_ros2_control
arm + gripper joint interfaces
Manipulation supervisor
product cycle + attach / detach proof
Composite Xacro loads the KUKA KR6 R900-2 model, gripper, camera and optional product
Factory attachment mode uses Gazebo detachable-joint and contact interfaces
The cycle supervisor coordinates navigation, manipulation actions, cancellation and status
Sources: src/amr_manipulation/launch/move_group.launch.py; src/amr_description/urdf/phase14_mobile_manipulator.urdf.xacro
15
Notes: Purpose: explain why MoveIt is separate from Nav2.
MoveIt2 runs move_group with the composite robot description and an OMPL planning pipeline. It plans arm and gripper trajectories against a planning scene that includes the robot, collision objects and product attachment state. gz_ros2_control exposes the simulated arm and gripper joint interfaces.
The manipulation supervisor coordinates product actions, attachment and detachment proof and cancellation. MoveIt does not publish the mobile base velocity command; Nav2 and command arbitration retain that authority.
Source basis: src/amr_manipulation/launch/move_group.launch.py; src/amr_description/urdf/phase14_mobile_manipulator.urdf.xacro; src/amr_manipulation/src

## Slide 16
AMR ROS 2 SOFTWARE ARCHITECTURE
Factory mission cycle
A factory task crosses navigation and manipulation boundaries. Each transition needs state, ownership and completion evidence
1
Select mode
autonomous + registry
2
Navigate
pickup station
3
Pick up
tag + MoveIt + attach
4
Transport
Nav2 + RPP
5
Dispatch
release + verify
6
Finish
status / home proof
KEY ACTION INTERFACES
/amr/factory/run_sequence
bounded product sequence
/amr/factory/transport_product
factory supervisor transport action
/amr/manipulation/execute_product_cycle
cycle manipulation action
/amr/mission/navigate_to_pose
navigation action
Sources: src/amr_bringup/config/interface_ownership.yaml; src/amr_factory/launch/factory_autonomous.launch.py; src/amr_manipulation
16
Notes: Purpose: explain how navigation and manipulation become one factory operation.
The supervisor selects autonomous mode, navigates to a pickup station, detects and picks up the product, transports it with Nav2 and RPP, dispatches it, verifies the terminal state and requests home only when the home preconditions are satisfied.
The action interfaces show the boundaries: run_sequence and transport_product belong to the factory supervisor, execute_product_cycle belongs to manipulation, and navigate_to_pose belongs to mission navigation.
Key point: correctness depends on state transitions and terminal proof across multiple nodes, not just on reaching a pose.
Source basis: src/amr_bringup/config/interface_ownership.yaml; src/amr_factory/launch/factory_autonomous.launch.py; src/amr_factory/src/factory_supervisor_node.cpp; src/amr_manipulation/src

## Slide 17
AMR ROS 2 SOFTWARE ARCHITECTURE
Third-party packages and project plugins
The system combines established ROS 2 packages with project-owned adapters, controllers and acceptance gates
THIRD-PARTY / OPEN SOURCE
ROS 2 Humble, Gazebo Harmonic, ros_gz_bridge
Nav2, robot_localization and SLAM Toolbox
MoveIt 2 and moveit_configs_utils
AprilTag ROS, tf2 and sensor / geometry message packages
gz_ros2_control and the KUKA support description
PROJECT-OWNED EXTENSIONS
HeadingLatchedRPP and FinalPositionRPP controller plugins
PrecisionNavfnPlanner and ExactGoalLattice planner plugins
Sensor adapters, point-cloud freshness gates and ownership contract
Command arbitration and native Gazebo command watchdog
Mission, factory and manipulation supervisors
Package count note: colcon discovers legacy, evidence, vendored and primary packages. Present the 17 packages under src/ as the primary project set; do not treat every colcon entry as a product node.
Sources: src/README.md; package.xml files; plugin XML files; colcon list (current workspace)
17
Notes: Purpose: separate external foundations from project-owned behavior.
Third-party foundations include ROS 2 Humble, Gazebo Harmonic, ros_gz_bridge, Nav2, robot_localization, SLAM Toolbox, MoveIt2, AprilTag ROS, tf2, message packages, gz_ros2_control and the KUKA support description.
Project-owned extensions include the custom RPP plugins, precision planner plugins, sensor adapters and freshness gates, command arbitration, the native command watchdog and the mission, factory and manipulation supervisors.
Package-count caution: colcon also discovers legacy, evidence and vendored packages. The primary product set is the 17 packages under src/.
Source basis: src/README.md; package.xml files; plugin XML files; current colcon list

## Slide 18
AMR ROS 2 SOFTWARE ARCHITECTURE
Project difficulties and reliability risks
The hardest part is coordinating time, geometry, lifecycle and authority across a distributed ROS 2 graph
Time and freshness
Simulated /clock, future TF, stale scans and bounded source timeouts
Single ownership
One publisher for each command and TF boundary; mode-dependent map → odom
Geometry and collision
Full rectangular footprint, docking endpoints, inflation and sensor self-visibility
Startup and lifecycle
Gazebo, adapters, Nav2, AMCL / SLAM and MoveIt must reach a usable state in order
Cancellation and proof
Stop, cancel, retreat, attachment, home permission and terminal status need evidence
Build and unit tests are necessary, but they do not prove simulation runtime acceptance. Runtime gates must observe fresh topics, TF ownership, collision behavior and terminal state.
Sources: AGENTS.md; .codex/DEBUG_PLAYBOOK.md; SESSION_HANDOFF.md; current runtime contracts
18
Notes: Purpose: give the audience a concrete explanation of why the project is difficult.
Time and freshness matter because ROS uses simulated time and stale or future data can make a pose look valid when it is not. Single ownership matters because duplicate TF or command publishers create ambiguous behavior. Geometry matters because the planner must respect the full rectangular footprint, not only the robot center. Startup and lifecycle matter because Gazebo, adapters, Nav2, localization and MoveIt must reach usable states in order. Cancellation and proof matter because stop, retreat, attachment, home and terminal status cross node boundaries.
Key point: build and unit tests are necessary but cannot replace runtime evidence.
Source basis: AGENTS.md; .codex/DEBUG_PLAYBOOK.md; SESSION_HANDOFF.md; current runtime contracts

## Slide 19
AMR ROS 2 SOFTWARE ARCHITECTURE
Current status and presentation guardrails
This deck describes the current source tree. Runtime acceptance remains a separate, dated evidence question
LATEST HANDOFF STATUS
Native41 AMCL private Product A proof is recorded as passed
Product B, return-home, strict/final acceptance and teardown remain pending
Functional recovery comes before later stability tuning
Product 103, Gate 7, hardware and functional-safety acceptance remain excluded
FACTS USED IN THIS DECK
Current planner config: SmacPlannerLattice plus project precision plugins
Current inflation radius: 0.75 m in planner and controller costmaps
Historical report values such as NavFn and 0.55 m are labeled historical
This presentation is a separate artifact, not an operator authority document
Verified anchors
src/amr_navigation/config/planner.yaml
src/amr_mpc_controller/config/controller.yaml
src/amr_slam/config/mapper.yaml
src/amr_localization/config/ekf.yaml
src/amr_bringup/config/interface_ownership.yaml
Use the dated SESSION_HANDOFF and live runtime evidence for acceptance claims.
Use this deck for architecture, interfaces and current implementation behavior.
Source: SESSION_HANDOFF.md (2026-10-04); current source configuration files; prior presentation audit
19
Notes: Purpose: close with the current status and prevent historical details from being repeated as current facts.
State clearly: the latest handoff records Native41 private Product A proof as passed, while Product B, return-home, strict/final acceptance and teardown remain pending. Functional recovery comes before later stability tuning.
Explain the historical-value guardrail: the current planner configuration uses SmacPlannerLattice plus project precision plugins, and current inflation is 0.75 m. Older presentation notes that mention NavFn or 0.55 m describe an older snapshot.
Use SESSION_HANDOFF and dated runtime evidence for acceptance claims. Use this deck to explain architecture and current implementation behavior.
Source basis: SESSION_HANDOFF.md dated 2026-10-04; src/amr_navigation/config/planner.yaml; src/amr_mpc_controller/config/controller.yaml; src/amr_slam/config/mapper.yaml; src/amr_localization/config/ekf.yaml; src/amr_bringup/config/interface_ownership.yaml