## Slide 1
ROS 2 Software Architecture
Autonomous mobile manipulator software stack
ROS 2 Humble | Gazebo Harmonic | Nav2 | MoveIt
Software scope only
Sensing
State
Planning
Authority
Motion
Typed interfaces connect intent to controlled execution
Notes: Open by defining the software scope. The project uses ROS 2 as a typed distributed graph. Navigation and manipulation request work, while one gated command path decides whether base motion reaches the simulator. Hardware and mechanical design are outside this presentation.
Sources:
- docs/ROS2_SOFTWARE_PRESENTATION_REPORT.md
- src/README.md

## Slide 2
System structure and package ownership
17 ROS 2 packages grouped by software responsibility
02
Contracts + policy
amr_interfaces | amr_bringup
Model + simulation boundary
amr_description | amr_simulation
Adapters + state
amr_sensor_adapters | amr_base_adapter | amr_localization | amr_perception
Mapping + navigation
amr_slam | amr_navigation | amr_mpc_controller | amr_mission
Authority + application
amr_control | amr_health | amr_exploration | amr_factory | amr_manipulation
External stacks
Nav2
robot_localization
SLAM Toolbox + AMCL
MoveIt
AprilTag ROS
ros_gz_bridge
Legacy source
amr_machine_controller
not an active package
Notes: Use the layers to connect package names to responsibilities. Packages either define project code and interfaces or configure external ROS 2 components. The orphan amr_machine_controller source has no package manifest or CMake entry, so it does not belong to the active graph.
Sources:
- src/README.md
- src/amr_bringup/config/interface_ownership.yaml
- docs/ROS2_SOFTWARE_PRESENTATION_REPORT.md sections 4, 5, and 12

## Slide 3
ROS 2 interfaces and communication
Names, types, QoS and ownership form the public contract
03
TOPIC
Continuous stream
/amr/localization/
odometry
nav_msgs/Odometry
SERVICE
Bounded request / response
/amr/factory/
set_operation_mode
amr_interfaces/
SetOperationMode
ACTION
Goal + feedback + result + cancel
/amr/factory/
run_sequence
amr_interfaces/RunSequence
LIFECYCLE
Controlled startup
configure -> inactive -> active
adapters, estimation, Nav2
DDS discovery + compatible QoS
Project status
BaseStatus | HealthStatus | ManipulatorStatus | FactoryStatus
Standard data
Twist | TwistStamped | Odometry | LaserScan | PointCloud2 | Imu | OccupancyGrid | Path
Notes: Explain why the project uses each interface style. Topics carry streams, services handle short requests, and actions retain state for long-running work. DDS matches endpoint names and types, while QoS controls reliability, durability, queue depth, deadline and lifespan. Status messages also carry boot IDs, sequences and validity so consumers can reject stale evidence.
Sources:
- src/amr_interfaces
- src/amr_interfaces/include/amr_interfaces/qos_profiles.hpp
- src/amr_bringup/config/interface_ownership.yaml

## Slide 4
Gazebo, ros_gz_bridge, RViz2 and adapters
Simulation-specific endpoints become stable project interfaces
04
GAZEBO HARMONIC
world + sensors + joints + odometry + base endpoint
ros_gz_bridge
message conversion
Lifecycle adapters
/amr/sensors/*
/amr/base/*
Consumers
localization | perception
SLAM | Nav2 | AprilTag
RViz2
map | TF | RobotModel | scans | clouds | paths
visualization only
Product camera adapter
exact image / CameraInfo timestamp match
640 x 480
Factory acceptance runs headless; sensors.rviz is optional
Notes: Gazebo publishes native simulation endpoints. ros_gz_bridge converts them into ROS 2 messages. The project adapters then create stable names under /amr so downstream nodes do not depend on the simulator's native names. RViz2 subscribes to graph data for inspection and has no accepted velocity authority.
Sources:
- src/amr_simulation/launch/amr_simulation.launch.py
- src/amr_simulation/rviz/sensors.rviz
- src/amr_sensor_adapters
- src/amr_factory/launch/factory_localization.launch.py

## Slide 5
Localization and TF ownership
Sensor fusion estimates motion; TF connects global, local and sensor frames
05
ESTIMATION
wheel joint states
wheel_odometry_node
/amr/localization/
wheel_odometry
IMU
/amr/sensors/imu/
data_raw
robot_localization EKF
30 Hz | two-dimensional mode
/amr/localization/
odometry
odom -> base_footprint
TF TREE
map
odom
base_footprint
base_link
lidars | IMU | camera | arm
SLAM Toolbox (mapping)
or AMCL (factory)
EKF
robot_state_publisher (static tree)
Notes: Wheel odometry integrates named wheel joint positions, while the EKF fuses wheel velocity and IMU information. The EKF is the only owner of odom to base_footprint. Mapping mode uses SLAM Toolbox for map to odom; factory localization uses AMCL. robot_state_publisher creates the fixed body and sensor tree from URDF.
Sources:
- src/amr_localization/src/wheel_odometry_node.cpp
- src/amr_localization/config/ekf.yaml
- src/amr_description/urdf/amr.urdf.xacro
- src/amr_bringup/config/interface_ownership.yaml

## Slide 6
Nav2 navigation pipeline
Mission intent becomes a bounded controller request
06
Mission supervisor
validates planar goal
NavFn planner
global path
Simple Smoother
refined path
RPP controller
path following
/amr/mpc/
cmd_vel
geometry_msgs/Twist
Map + global costmap
front + rear PointCloud2
Current controller profile
0.5 m/s
desired speed
0.3–0.9 m
lookahead range
1.5 s
lookahead time
1.2 x 0.8 m
software footprint
amr_mpc_controller is compatibility naming; the active algorithm is Regulated Pure Pursuit
Notes: The mission supervisor exposes the project navigation actions and coordinates Nav2 clients. NavFn computes the path, Simple Smoother refines it, and RPP produces the upstream Twist request. Costmaps combine the map, robot footprint and front/rear perception data. This is a request path, not the final authority path.
Sources:
- src/amr_mission/src/mission_supervisor_node.cpp
- src/amr_navigation/config/planner.yaml
- src/amr_mpc_controller/config/controller.yaml

## Slide 7
MoveIt and factory orchestration
Factory actions compose navigation and manipulation into a product cycle
07
Operator / CLI
Factory supervisor
registry + queue + status
Mission + Nav2
station navigation
Cycle supervisor
ExecuteProductCycle
MoveIt move_group
arm planning + execution
Public factory interfaces
TransportProduct | RunSequence | NavigateStation | SetOperationMode | stop / cancel
Evidence gates
tag identity + five stable observations + contact freshness + pose tolerance + attachment state
Autonomous scope
Product 101 + Product 102
Product 103 remains disabled
Notes: The factory supervisor loads the product and station registries, validates them and owns the high-level action results. Navigation reaches stations through the mission boundary. The cycle supervisor coordinates the manipulation stage, and MoveIt plans arm trajectories. Evidence gates prevent a cycle from accepting inconsistent tag, contact, pose or attachment data.
Sources:
- src/amr_factory/src/factory_supervisor_node.cpp
- src/amr_factory/config/products.yaml
- src/amr_factory/config/stations.yaml
- src/amr_manipulation/scripts/cycle_manipulation_supervisor.py
- src/amr_manipulation/launch/move_group.launch.py

## Slide 8
Command authority and fail-closed motion
Every layer must prove that a velocity request remains admissible
08
Nav2 request
Twist
COMMAND ARBITRATION
freshness | planar validity
manipulator permission
base readiness | limits
/amr/control/
cmd_vel
TwistStamped
Base adapter
revalidate + zero stale
Bridge + Gazebo
watchdog expiry
Sole project-owned velocity publisher
20 Hz
arbitration output
200 ms
command timeout + lifespan
0.5 m/s
linear limit
0.4 rad/s
angular limit
0.025 m/s
nominal change per tick
Missing, stale, invalid or contradictory evidence stops or rejects motion
Notes: Separate planning from authority. Nav2 publishes an upstream request. The arbitration node checks freshness, semantics, interlocks and rate limits, then publishes the only project-owned accepted base velocity. The base adapter performs another finite and planar check. The Gazebo watchdog provides independent native command expiry. Health status only reports observations and cannot enable motion.
Sources:
- src/amr_control/src/command_arbitration_node.cpp
- src/amr_base_adapter/src/base_adapter_node.cpp
- src/amr_simulation/src/command_watchdog_system.cpp
- src/amr_interfaces/include/amr_interfaces/qos_profiles.hpp

## Slide 9
Theory and project calculations
Current software parameters explain odometry, timing and navigation geometry
09
DIFFERENTIAL DRIVE
v = r/2 (omega_L + omega_R)
omega = r/L (omega_R - omega_L)
r = 0.1128 m L = 0.566 m
Equal +1 rad wheel motion
Delta s = 0.1128 m
Delta theta = 0
Opposite +/-1 rad motion
Delta s = 0
Delta theta = 0.3986 rad
Source: diff_drive.hpp
NAVIGATION GEOMETRY
100 x 100 cells
5 m local costmap / 0.05 m resolution
11 cells
0.55 m inflation / 0.05 m resolution
0.75 m
RPP: 0.5 m/s x 1.5 s lookahead time
0.025 m/s per tick
0.5 m/s² acceleration x 0.05 s at 20 Hz
Notes: Connect each equation to a software component. Differential-drive midpoint integration produces wheel odometry. Costmap resolution determines memory geometry and inflation width. RPP scales lookahead with speed. The arbitration timer and acceleration limit determine the nominal per-tick command change. These are explanatory calculations from current parameters, not new thresholds.
Sources:
- src/amr_localization/include/amr_localization/diff_drive.hpp
- src/amr_navigation/config/planner.yaml
- src/amr_mpc_controller/config/controller.yaml
- src/amr_control/src/command_arbitration_node.cpp

## Slide 10
Current software state
Implemented source and remaining runtime evidence are separate claims
10
IMPLEMENTED IN SOURCE
PENDING EVIDENCE
Typed public interfaces and ownership registry
Adapters, localization, perception and TF model
Nav2 RPP pipeline and command arbitration
Factory cycles for Product 101 and 102
Fail-closed freshness and interlock gates
Fresh Phase 15 mapping runtime proof
Live per-edge TF ownership and freshness proof
Quantitative map-quality acceptance
Candidate-map promotion and canonical replacement
Hardware and functional-safety acceptance
Contract gap: /amr/mission/navigate_to_pose_retreat exists in source but is absent from the ownership registry
Typed interfaces + explicit ownership + gated motion
Notes: Close by distinguishing implementation from runtime proof. The source tree contains the architecture and current Product 101/102 factory scope. Phase 15 still needs a fresh runtime mapping run, per-edge TF evidence, map-quality acceptance and explicit promotion. The ownership registry also needs the source-defined retreat action. Do not claim hardware or functional-safety acceptance.
Sources:
- SESSION_HANDOFF.md
- docs/PHASE_15_FACTORY_SLAM_COMMISSIONING.md
- src/amr_bringup/config/interface_ownership.yaml
- src/amr_mission/src/mission_supervisor_node.cpp